## Slide 1: E-Governance Infrastructure – Data Centers

## Slide 2: Data Centers
A View of Data Center

## Slide 3: A Data Center
Data centers are highly secure, fault-resistant facilities housing equipment that connect to telecommunications networks.
The facilities accommodate servers, switches, routers, modem racks.
Data centers support corporate databases, websites and provide locations for service providers (e.g. ISP, ASP), Web hosting companies, and other IT services.
A standard for measuring equipment space in a data center is Rack Location Units (RLUs)

## Slide 4: Data Center Components
Basic Data Center facility systems:
  Physical space
  Raised flooring
  In-room electrical
  Standby power
  Data cabling
  Cooling
  Fire suppression

## Slide 5: Data Center Design Criteria
How many layers of infrastructure should your Data Center possess?
Will it be the only server environment for your company or one of several?
Will the room house production servers and be a business-critical site or contain a minimum of equipment for disaster recovery purposes and serve as a failover location?
How long is its initial construction expected to meet your company's needs?
What is it all going to cost?

## Slide 6: Data Center Design Criteria
Availability
Infrastructure Tiers
One Room or Several?
Life Span
Budget Decisions

## Slide 7: Data Center Design Criteria
Availability:
  The degree to which Data Center devices function continuously is known as the room's availability or its uptime.
  Availability is represented as a percentage of time.
  How many days, hours, and minutes is the Data Center's electrical infrastructure operational and supplying power over a given time period

## Slide 8: Data Centre Availability

## Slide 9: Data Center Design Criteria
Infrastructure Tiers
  The higher the availability you want your Data Center to achieve, the more layers of infrastructure it must have.
  N capacity is the amount of infrastructure required to support all servers or networking devices in the Data Center, assuming that the space is filled to maximum capacity and all devices are functioning.
  N most commonly used when discussing standby power, cooling, and the room's network.
  N+1 infrastructure can support the Data Center at full server capacity and includes an additional component
  Alternately called a 2N or system-plus-system design, it involves fully doubling the required number of infrastructure components
  Even higher tiers exist or can be created: 3N, 4N, and so on.

## Slide 10: Data Center Design Criteria
One Room or Several?
  One large Data Center is simpler to manage than several smaller ones.
  Having only one server environment puts all of your eggs in one basket.

## Slide 11: Data Center Challenges
Traffic load balance
Support for virtual machine (VM) migration
Achieving bisection bandwidth
Power savings / Cooling
Network management (provisioning)
Security (dealing with multiple tenants)

## Slide 12: Common Data Center Topology
Internet
Servers
Layer-2 switch
Access
Data Center
Layer-2/3 switch
Aggregation
Layer-3 router
Core
Notes: Before describing the problems with current middlebox deployment approaches, let me first describe the commonly used 3-tier data center network topology. At the top is the core-tier, whose layer-3 routers connect the data center to the Internet or to the rest of the campus network. At the bottom is the access tier, containing the layer-2 switches into which servers are plugged in.
In between the access and core tiers are the layer 2/3 switches of the aggregation tier. Middleboxes are commonly deployed at the aggregation tier.
Multiple redundant links connect together the various switches and servers. To prevent forwarding loops, we use mechanisms like spanning tree construction to block out some of the links. For example, the topology as shown here.

## Slide 13: Data Center Network Topology
CR
CR
AR
AR
AR
AR
. . .
S
S
Internet
S
S
A
A
A
…
S
S
A
A
A
…
. . .
Key
CR = Core Router
AR = Access Router
S = Ethernet Switch
A = Rack of app. servers
~ 1,000 servers/pod

## Slide 14: Requirements for future data center
To catch up with the trend of mega data center, DCN technology should meet the requirements as below
  High Scalability
  Transparent VM migration (high agility)
  Easy deployment requiring less human administration
  Efficient communication
  Loop free forwarding
  Fault Tolerance
Current DCN technology can’t meet requirements.
  Layer 3 protocol can not support the transparent VM migration.
  Current Layer 2 protocol is not scalable due to the size of forwarding table and native broadcasting for address resolution.

## Slide 15: Problems with Common Topologies
Single point of failure
Over subscription of links higher up in the topology
Tradeoff between cost and provisioning

## Slide 16: Reminder: Layer 2 vs. Layer 3
Ethernet switching (layer 2)
  Cheaper switch equipment
  Fixed addresses and auto-configuration
  Seamless mobility, migration, and failover
IP routing (layer 3)
  Scalability through hierarchical addressing
  Efficiency through shortest-path routing
  Multipath routing through equal-cost multipath
So, like in enterprises…
  Data centers often connect layer-2 islands by IP routers

## Slide 17: Need for Layer 2
Certain monitoring apps require server with same role to be on the same VLAN
Using same IP on dual homed servers
Allows organic growth of server farms
Migration is easier

## Slide 18: Review of Layer 2 & Layer 3
Layer 2
  One spanning tree for entire network
    Prevents loops
    Ignores alternate paths
Layer 3
  Shortest path routing between source and destination
  Best-effort delivery
Notes: In this talk, I shall next explain the problems with current middlebox deployment mechanisms.
I shall then describe how our solution, the policy-aware switching layer simplifies middlebox deployment and achieves the properties I mentioned earlier.
I shall briefly discuss related work, and our prototype implementation and evaluation of the policy-aware switching layer.

## Slide 19: Data Center Traffic Engineering
Challenges and Opportunities

## Slide 20: Wide-Area Network
Router
Router
DNS Server
DNS-based
site selection
. . .
. . .
Servers
Servers
Internet
Clients
Data Centers

## Slide 21: Wide-Area Network: Ingress Proxies
Router
Router
Data Centers
. . .
. . .
Servers
Servers
Clients
Proxy
Proxy

## Slide 22: Traffic Engineering Challenges
Scale
  Many switches, hosts, and virtual machines
Churn
  Large number of component failures
  Virtual Machine (VM) migration
Traffic characteristics
  High traffic volume and dense traffic matrix
  Volatile, unpredictable traffic patterns
Performance requirements
  Delay-sensitive applications
  Resource isolation between tenants

## Slide 23: Traffic Engineering Opportunities
Efficient network
  Low propagation delay and high capacity
Specialized topology
  Fat tree, Clos network, etc.
  Opportunities for hierarchical addressing
Control over both network and hosts
  Joint optimization of routing and server placement
  Can move network functionality into the end host
Flexible movement of workload
  Services replicated at multiple servers and data centers
  Virtual Machine (VM) migration

## Slide 24
State Data Centre (SDC) has been identified as one of the important element of the core infrastructure for supporting e-Governance initiatives of National eGovernance Plan (NeGP).
Under NeGP, it is proposed to create State Data Centres for the States to consolidate services, applications and infrastructure to provide efficient electronic delivery of G2G, G2C and G2B services. These services can be rendered by the States through common delivery platform seamlessly supported by core Connectivity Infrastructure such as State Wide Area Network (SWAN) and Common Service Centre (CSC) connectivity extended up to village level. State Data Centre would provide many functionalities and some of the key functionalities are Central Repository of the State, Secure Data Storage, Online Delivery of Services, Citizen Information/Services Portal, State Intranet Portal, Disaster Recovery, Remote Management and Service Integration etc. SDCs would also provide better operation & management control and minimize overall cost of Data Management, IT Resource Management, Deployment and other costs.
Department of Information Technology (DIT) has formulated the Guidelines to provide Technical and Financial assistance to the States for setting up State Data Centre. These Guidelines also include the implementation options that can be exercised by the State to establish the SDC.

## Slide 25
State Data Centre (SDC) has been identified as one of the important element of the core infrastructure for supporting e-Governance initiatives of National eGovernance Plan (NeGP).
Under NeGP, it is proposed to create State Data Centres for the States to consolidate services, applications and infrastructure to provide efficient electronic delivery of G2G, G2C and G2B services. These services can be rendered by the States through common delivery platform seamlessly supported by core Connectivity Infrastructure such as State Wide Area Network (SWAN) and Common Service Centre (CSC) connectivity extended up to village level. State Data Centre would provide many functionalities and some of the key functionalities are Central Repository of the State, Secure Data Storage, Online Delivery of Services, Citizen Information/Services Portal, State Intranet Portal, Disaster Recovery, Remote Management and Service Integration etc. SDCs would also provide better operation & management control and minimize overall cost of Data Management, IT Resource Management, Deployment and other costs.
Department of Information Technology (DIT) has formulated the Guidelines to provide Technical and Financial assistance to the States for setting up State Data Centre. These Guidelines also include the implementation options that can be exercised by the State to establish the SDC.

## Slide 26: National Panchayat Portal (http://panchayat.nic.in)
73rd Amendment Act enacted in 1992 to enhance the democratic set up by establishing the third-tier of the government, the Panchayati Raj Insitutions (PRIs) to work at district-, block- and village- levels
Ministry of Panchayati Raj (MoPR), Government of India formed in 2004 to work for the effective implementation of Panchayati Raj or local self governance in the country
There are about: 31 State Panchayat Raj Departments , 536 District Panchayats or Zilla Parishads (ZPs), 6096 Block Panchayats/Intermediate Panchayats (BPs/IPs) and 2,40,000 Gram panchayats/Village Panchayats (GPs/VPs)

## Slide 27: Challenges of Information Dissemination & Management
The sheer no. of portals to be created and maintained is mind boggling
Maintenance of the web site
  Lack of technical skills to manage and maintain web sites
  Lack of proper review and approval mechanism,
  Inconsistency in the information published through different media
Linguistic diversity
Remoteness of the institutions
Poor Network Connectivity

## Slide 28: NPP–Collaborative Portal Generation
Dynamically generates portals for Ministry of Panchayati Raj, all 35 State Panchayati Raj departments, all 560 district panchayats, 6096 intermediate panchayats and 2,40,000 village panchayats in the country
Portal site acts as a window to information & services provided by the respective PRI
Portals tailored for respective PRI in terms of: Page Layout, Content Presentation, Language, Visual Theme
The portals can collaborate with one another to share the resources of the framework such as content, page layout, visual theme, etc.

## Slide 29: NPP – Content Presentation & Organization
Portal Pages- A PRI portal site may present content in more than one web page format called portal page to cater to different sections of the citizen or different focus areas of the community. For eg., Farmer’s page, Health Page, Student’s Page
    Portlets - Each portal page is divided up into sections called portlets, e.g. Content Portlets , Navigation Portlets and Opinion Portlets

## Slide 30: NPP – Language Support
Each PRI portal site could use one or more languages used by its community
UNICODE standards-based
  Hindi, English and other regional languages (which have been UNICODE enabled)
  Easier to mix languages, share with others
Multiple language support on each portal site
Easy switching to another language supported by the site without disconnecting from the site
User-friendly screens to add or customize a language version as per local needs

## Slide 31: NPP – Powerful Search Facility
Simple Search: by word or phrase (exact or any word)
Metadata-based search: based on Dublin-Core metadata tags used to define the content such as subject, author, date published or status etc.
Search in title, abstract, typed text or attached files (doc, pdf,ppt etc.) of the content item
Search across multiple languages supported by the site

## Slide 32: NPP – Visual Themes
A visual theme defines the colour scheme, header images, logos etc.
Each PRI can define its own theme
The theme for a PRI portal site can be set simply by selecting a theme for the site
PRIs can exchange themes amongst themselves

## Slide 33: User Management
Role-based Privileges
  Viewer
  Contributor
  Editor
  Content Manager
  Site Designer
  User Manager
  System Administrator
NPP provides two user groups by default: citizen, operator and manager
Each PRI could use the default user groups or create their own user groups as per their need

## Slide 34: NPP - Authentication
General public need not login to browse the information provided by the portal site
General public can, however, self-register as citizens to take advantage of facilities provided by portal site for authenticated users such as messaging facility
PRI officials must login if they want to do more than just browse the site.

## Slide 35: NPP – Content Management
Content Creation
Content Editing & Versioning
Content Publishing
Content Indexing
Garbage Management
Content Flow Management

## Slide 36: NPP – Collaborative Content Management
Each site could be configured to allow content flow across various users to ensure that the content is appropriately edited, approved and then published.
Currently, each site has two types of users: operator and manager
  Operator can create and edit content
  Manager can edit content created by operators as well as self
  Only managers can publish content
Operator
Manager
Content
Edit/ Approve
Publish

## Slide 37: NPP - Messaging
Provides message facility to send 'mails' between users of different PRI sites.
This could be used by citizens to send messages to one another as well as to PRI officials and vice versa, without a need to access an e-mail server and Internet
Users may belong to different PRI portal sites which may be distributed across systems
Similar to e.g. Yahoo mail, but works without Internet.

## Slide 38: NPP – Future Directions
NPP – A semantic Web Portal
  Already, NPP captures metadata related to content.
  Further, some basic common classification has been achieved by standardizing on subject areas and types of content (which are same for all government agencies). This gives capability to search across languages in a given subject area or type of content
  It is proposed to semantically enhance the current search capability of NPP by linking it to domain ontology
  This would enable users to query for information or services across portal sites and across languages using any domain-specific concept
  Further, it is proposed to enhance the portal framework as an ontology-building tool